PROPOSAL FOR DRAFT 06 SERIES OF AMENDMENTS

TO REGULATION No. 83 (English text)

##### Transmitted by the Expert from Norway

#### A.	PROPOSAL

Paragraph 5.2., table 1 referred to correct to read (new wording underlined, old wording crossed out):

“Table 1

Different routes for type approval and extensions

| Type approval test | Positive-ignition engined vehicles of categories M and N | Compression-ignition engined vehicles of categories M1 and N1 |
| --- | --- | --- |
| Type I | YES (maximum mass ( 3.5 t) | YES (maximum mass ( 3.5 t) |
| Type II | YES (maximum mass > 3.5 t) | -- |
| Type III | YES | -- |
| Type IV | YES (maximum mass ( 3.5 t) | -- |
| Type V | YES (maximum mass ( 3.5 t) | YES (maximum mass ( 3.5 t) |
| Type VI | YES (maximum mass ( 3.5 t) |  |
| On-board diagnostics | YES, in accordance with paragraph 11.1.5 | YES, in accordance with paragraph 11.1.5. |
| Extension conditions | Paragraph 7. | Paragraph 7, M2 and N2 category vehicles (reference mass ( 2,840 kg) |

“

Paragraph 5.3.5.1., correct to read (new wording underlined, old wording crossed out):

“5.3.5.1.	This test shall be carried out on all M1 and N1 Class I vehicles equipped with a positive-ignition engine.”

Paragraph 5.3.5.2., correct to read (new wording underlined, old wording crossed out):

“5.3.5.2.	Subject to the requirements in paragraphs 5.3.5.2.2. and 5.3.5.3. the test shall be performed three times. The resulting mass of carbon monoxide and hydrocarbon emission shall be less than the limits shown in the table below:

| Test temperature 266 K (-7ºC) |
| --- |
| Category | Class | Carbon monoxide L1, (g/km) | Hydrocarbons L2, (g/km) |
| M1 (1) | - | 15 | 1.8 |
| N1 | I | 15 | 1.8 |
| N1 (2) | II | 24 | 2.7 |
|  | III | 30 | 3.2 |
| (1) Except vehicles designed to carry more than six occupants and vehicles the maximum mass of which exceeds 2 500 kg. (2) And those category M1 vehicles which are specified in note 1. |

Paragraph 11.1.4.4., correct to read (new wording underlined, old wording crossed out):

“11.1.4.4.	As from 1 January 2002, the Type VI test defined in annex 8 is applicable to new types of vehicle of category M1 and of category N1 Class I and which are equipped with a positive-ignition engine. As from 1 January 2003, the Type VI test defined in annex 8 is applicable to new types of vehicle of category M1 equipped to carry more than six occupants (including the driver) or whose maximum mass exceeds 2,500 kg and of category N1 Class II and III and which are equipped with a positive-ignition engine.”

*     *     *

B.	JUSTIFICATION

Re. para. 11.1.5.1.:	Directive 2001/100/EC introduces limit values and entry into force dates for the low temperature test (-7ºC) for new types of passenger vehicles (M1) designed to carry more than six occupants and vehicles the maximum mass of which exceeds 2 500 kg and light duty (N1) vehicles class II and III and equipped with positive-ignition engines. For harmonization it is therefore proposed to amend the regulation according to the Directive.

__________