| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRSG/2004/13 13 July 2004 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on General Safety Provisions (GRSG)

(Eighty-seventh session, 12-15 October  2004,

agenda item 2.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 52

(Small capacity passenger vehicles, M2 and M3 category)

Transmitted by the expert from the United Kingdom

Note:  The text reproduced below was prepared by the expert from the United Kingdom.  It is based on the text of informal document No. GRSG-86-33 (TRANS/WP.29/GRSG/64, para. 7.) and supersedes document TRANS/WP.29/GRSG/2004/1.

____________

_______________

Note: This document is distributed to the Experts on General Safety Provisions only.

Paragraph 5.7.8.1., amend to read:

"5.7.8.1.	Over each seating position and, except in the case of the seat(s) alongside the driver, its associated foot space, there shall be measured a free space with a height of not less than 90 cm, measured from the highest point of the uncompressed seat cushion and at least 135 cm from the mean level of the floor in the foot space.  In the case of vehicles to which paragraph 5.7.1.9. applies, and also for seat(s) alongside the driver, these dimensions may be reduced to 120 сm, measured from the floor and 80 cm measured from the highest point of the uncompressed seat cushion."

______________