Draft proposal of corrigendum to Regulation No. 65

The text reproduced below was prepared by the expert from Germany on the base of the document  ECE – Regulation No. 65, Addendum 64, Revision 1 in order to insert a corrigendum because of a typing error in Annex 3 to this Regulation.  The modifications in Annex 3 to this Regulation are marked in bold characters

A 	PROPOSAL

Annex 3

TRICHROMATIC CO-ORDINATES FOR THE LIGHT EMITTED THROUGH THE AMBER OR BLUE FILTERS CONSTITUTING THE COVERS OF SPECIAL WARNING LAMPS

Under the conditions of paragraph 7 of this Regulation, the trichromatic co-ordinates of light emitted through the filters used for special warning lamps shall lie within the following boundaries:

1.	Amber (/

limit towards green	:	y  ≤ x – 0.120

limit towards red	:	y ( 0.390

limit towards white	:	y ( 0.790 - 0.670 x

- Blue

limit towards green	:		y = 0.065 + 0.805 x

limit towards white	:		y = 0.400 – x

There is a typing error in the following line:

limit towards purple	:		y = 0.133 + 0.600y

The correct reading is:				x = 0.133 + 0.600y

Or in the presentation as a function of y			y = 1.667x – 0.222

B.	JUSTIFICATION:

For the colour Blue the last formula comprises a typing error which must be corrected.