| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRRF/2007/21 13 July 2007 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Brakes and Running Gear

Sixty-second session

Geneva, 25-28 September 2007

Item 9(d) of the provisional agenda

REGULATION No. 106 (Pneumatic tyres for agricultural vehicles)

#### Proposal for draft amendments to Regulation No. 106

Submitted by the experts from the European Tyre and Rim Technical Organisation (ETRTO)

The text reproduced below was prepared by the experts from ETRTO to amend Annex 5 of Regulation No. 106 with a view to specifying some dimensional data for code designated tyre size designations as well as additional tyre sizes, to cover tyre versions and types, existing on the market, that were omitted when compiling tables in Annex 5.  The proposal also aims at deleting some sizes from Annex 5, table 7, as those tyres are generally classified 'All Terrain Vehicle' tyres, not specifically for equipment of agricultural and forestry machines, that have a speed symbol F (80 km/h) exceeding the scope of the Regulation.  The modifications to the existing text of the Regulation are marked in bold characters or as strikethrough.

A.	PROPOSAL

Annex 5

Table 5 (1 of 2), insert a new column for "Overall diameter (D)" identified by (*), and add in the new column the relevant values for the following tyre size designations:

"Table 5 (1 of 2) Agricultural Implement Tyres – Normal section Sizes

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 4.00 – 8 IMP | 3 | 112 | 418 | 425 | 203 |
| 4.00 – 9 IMP | 3 | 112 | 443 | 460 | 229 |
| 4.00 – 12 IMP | 3 | 112 | 519 | 536 | 305 |
| 4.00 – 15 IMP | 3 | 112 | 595 | 612 | 381 |
| 4.00 – 18 IMP | 3 | 112 | 672 | 688 | 457 |
| 4.50 – 19 IMP | 3 | 124 | 720 | 733 | 483 |
| 4.80 – 8 IMP | 3,75 | 121 | 423 | 449 | 203 |
| 5.0 – 10 IMP | 4 | 145 | 505 | 517 | 254 |
| 5.00 – 15 IMP | 3 | 130 | 639 | 655 | 381 |
| 5.50 – 16 IMP | 4 | 150 | 685 | 703 | 406 |
| 5.90 – 15 IMP | 4 | 150 | 665 | 681 | 381 |
| 6.00 - 9 IMP | 4,5 | 169 | 543 | 556 | 229 |
| 6.00 – 16 IMP | 4 | 158 | 712 | 729 | 406 |
| 6.50 – 16 IMP | 4,5 | 173 | 735 | 754 | 406 |
| 6.70 – 15 IMP | 4,5 | 182 | 733 | 720 | 381 |
| 7.00- 12 IMP | 5 | 187 | 667 | 685 | 305 |
| 7.50 – 10 IMP | 6 | 214 | 634 | 649 | 254 |
| 7.50 – 16 IMP | 5,5 | 202 | 785 | 801 | 406 |
| 7.50 – 18 IMP | 5,5 | 202 | 836 | 852 | 457 |
| 7.50 – 20 IMP | 5,5 | 202 | 887 | 903 | 508 |
| 7.50 – 24 IMP | 5,5 | 202 | 989 | 1013 | 610 |
| 7.60 – 15 IMP | 5,5 | 193 | 734 | 751 | 381 |
| 13.50 – 16.1 IMP | 11 | 353 | 1021 | 1043 | 409 |

"

Table 5 (1 of 2), insert the following new tyre size designations:

"

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 4.10/3.50-4 IMP | 2.10 | 89 | 272 |  | 101 |
| 190-8 IMP | 5.50 | 182 | 430 |  | 203 |

"

After table 5 (1 of 2), add the following notes to read:

"Notes:	1.	The suffix "IMP" may be replaced by the wording "IMPLEMENT" on the tyre sidewall.

2.	Tyres of radial structure are identified by means of the letter "R" in place of "-" (e.g. 7.5 L R 15).

3.	Overall diameters (D) in column (*) apply to tyres marked with classification code 'I-3' – see Annex 10)."

Table 6 (1 of 2), insert a new column for "Overall diameter (D)" identified by (*), and add in the new column the relevant values for the following tyre size designations:

"Table 6 (1 of 2) Agricultural Implement Tyres – Low Section Sizes

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 8.5L – 14 IMP | 6 | 216 | 721 | 735 | 356 |
| 9.5L – 14 IMP | 7 | 241 | 741 | 757 | 356 |
| 9.5L – 15 IMP | 7 | 241 | 767 | 782 | 381 |
| 11L – 14 IMP | 8 | 279 | 752 | 770 | 356 |
| 11L – 15 IMP | 8 | 279 | 777 | 796 | 381 |
| 11L – 16 IMP | 8 | 279 | 803 | 821 | 406 |
| 12.5L – 15 IMP | 10 | 318 | 823 | 845 | 381 |
| 12.5L – 16 IMP | 10 | 318 | 848 | 870 | 406 |
| 16.5L – 16.1 IMP | 14 | 419 | 1024 | 1046 | 409 |

Table 6 (2 of 2), insert a new column for "Overall diameter (D)" identified by (*), and add in the new column the relevant values for the following tyre size designations:

"Table 6 (2 of 2) Agricultural Implement Tyres – Low Section Sizes

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 6.5/80 – 12 IMP | 5 | 163 | 569 | 588 | 305 |
| 6.5/80 – 15 IMP | 5 | 163 | 645 | 663 | 381 |
| 9.0/75 – 16 IMP | 7 | 226 | 749 | 770 | 406 |
| 10.0/80 – 12 IMP | 9 | 264 | 710 | 730 | 305 |
| 11.0/65 - 12 IMP | 9 | 281 | 670 | 692 | 305 |
| 10.0/75 - 15.3 IMP | 9 | 264 | 760 | 780 | 389 |
| 11.5/80 – 15.3 IMP IMP | 9 | 290 | 845 | 867 | 389 |
| 10.5/80 – 18 IMP | 9 | 274 | 885 | 907 | 457 |
| 12.0/75 - 18 IMP | 9 | 299 | 915 | 937 | 457 |
| 12.5/80 - 18 IMP | 9 | 308 | 965 | 987 | 457 |
| 14.5/80 - 18 IMP | 12 | 372 | 1060 | 1082 | 457 |
| 15.0/55 - 17 IMP | 13 | 391 | 850 | 872 | 432 |
| 15.5/80 - 24 IMP | 13 | 394 | 1240 | 1262 | 610 |
| 16.0/70 - 20 IMP | 14 | 418 | 1075 | 1097 | 508 |
| 16.5/85 - 24 IMP | 13 | 417 | 1322 | 1344 | 610 |
| 16.5/85 - 28 IMP | 13 | 417 | 1423 | 1445 | 711 |

"

After table 6 (2 of 2), add the following note 3. to read:

"3.	Overall diameters (D) in column (*) apply to tyres marked with classification code 'I-3' – see Annex 10)."

Table 7 (1 of 2), insert the following new tyre size designations:

"

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  | (mm) | (mm) | (mm) |
| 13x6.00-6 | 5 | 154 | 330 | 152 |
| 14x4.50-6 | 3,5 | 113 | 356 | 152 |
| 18x7.50-8 | 6 | 191 | 457 | 203 |
| 19x9.50-8 | 7,5 | 240 | 483 | 203 |
| 20x8.00-8 | 6,5 | 204 | 508 | 203 |
| 20x9.00-8 | 7 | 227 | 508 | 203 |
| 21x7.00-10 | 5,5 | 177 | 533 | 254 |
| 23x9.50-12 | 7 | 235 | 577 | 305 |
| 24x12.00-12 | 9,5 | 304 | 610 | 305 |
| 25x8.00-12 | 6,5 | 203 | 635 | 305 |
| 25x10.00-12 | 8 | 254 | 635 | 305 |
| 25x11.00-12 | 9 | 279 | 635 | 305 |

"

Table 7 (2 of 2), add the following new tyre size designations:

"

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  | (mm) | (mm) | (mm) |
| DH73x50.00-32 | 44 | 1270 | 1880 | 813 |

"

After table 6 (2 of 2), add the following note 3. to read:

"4.	Coefficient b for the calculation of the Overall diameter Dmax:

(a)	1.12 for tyres with Nominal rim Diameter (d) less than 380 mm;

(b)	1.10 for tyres with Nominal rim Diameter (d) 381 mm and above."

Table 7 (1 of 2), for the tyre size designation AT21x7–10, AT22x9–8, AT23x7–10, AT23x8–11, AT24x8–11, AT24x9–11, AT24x10–11, AT25x8–12, AT25x11–9 and AT25x11–10, the whole row should be deleted.

B.	JUSTIFICATION

Annex 5 of Regulation 106 lists theoretical rim, outer diameter and nominal section width of tyres of certain size designations for which calculations of dimensions as per paragraphs 6.1.1. and 6.2.1. are not applicable.  In fact, sizes listed in Annex 5 are subject to the specific requirements of paragraphs 6.1.2., 6.2.2. and 6.4.1.1.

Additional overall diameters for selected sizes requested for addition in tables 5 and 6 reflect existing standards for implement tyres having 'traction tread' (classification code I-3 as per Annex 10) and mainly conform to data published for many years in the Tire and Rim Association Inc. (T&RA) - Year Book and in the European Tyre and Rim Technical Organisation (ETRTO) Standards Manual, but which were inadvertently omitted when the tables were first approved.  Consequently, it is proposed to specify the additional marking 'I-3' as per the new footnote 3 to identify those sizes characterized by a larger overall diameter.

Ad hoc coefficients b for the calculation of max overall diameter for sizes listed in table 7 (as proposed with additional footnote 4) reflect standard data for "agricultural high flotation tyres", having a nominal rim diameter (d) 381 mm and above, and for "utility vehicle and lawn and garden tractor tyres", having a nominal rim diameter (d) lower than 380 mm, published since many years in the Tire and Rim Association Inc. (T&RA) - Year Book, but which were inadvertently omitted when the tables were first approved.

Additional tyre size designations in table 5 reflect data published in the Scandinavian Tire and Rim Organisation (STRO) Data Book and additional tyre size designations in table 7 reflect data published in the Tire and Rim Association Inc. (T&RA) - Year Book

The tyre size designations to be deleted from table 7 in actual facts cannot be classified as tyres for agricultural machinery as they are generally known as tyres for "All Terrain Vehicles" (hence the prefix AT in the tyre size designation) and allowed for speeds in excess of 80 km/h in conformity with the speed category symbol "F (80 km/h)", marked in the service description.

Speed category symbol "F" is outside of the scope of Regulation No. 106, which, at the present time, considers only tyres designed for agricultural and forestry machines classified with speed category symbol not exceeding "D (65 km/h)".

- - - - -