Proposal for draft amendments to Regulation No. 107

(M2 and M3 vehicles)

Note:	The text of the German proposal is marked in bold characters and the modifications by Hungarian expert are marked in bold italic characters.

A.	PROPOSAL

Annex 3,

Paragraph 7.6.2.7., amend to read:

7.6.2.7.	If escape hatches are fitted, they shall be positioned as follows:

(a)	If there is only one hatch in the case of Class I, II or III it shall be situated in the middle third of the vehicle;

(b)	If there are two hatches, they shall be located in the front and rear half of the vehicle being separated by a distance of at least 2 m measured between the nearest edges of the apertures in a line parallel to the longitudinal axis of the vehicle;

(c)	If there are more than two hatches, they shall be closely evenly distributed alongside the vehicle being separated by a distance of at last 2 m measured between the nearest edges of the apertures in line parallel to the longitudinal axis of the vehicle;

(d)	In vehicles Class A or B a single hatch shall be positioned in the centre area above the passenger compartment."

B.	JUSTIFICATION

Supporting the German proposal (GRSG-91-26) the expert from Hungary suggests adding two more subparagraphs to the German proposal to make the whole paragraph more general and more precise.

- - - - -