| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2008/105 23 July 2008 ENGLISH Original: ENGLISH AND FRENCH |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-sixth session

Geneva, 11 – 14 November 2008

Item 4.2.7 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 2 to the 05 series of amendments to Regulation No. 16

(Safety-belts)

Submitted by the Working Party on Passive Safety (GRSP) (/

The text reproduced below was adopted by GRSP at its forty-third session.  It is based on ECE/TRANS/WP.29/GRSP/2007/3, part A.1, as amended by paragraph 34 of the report.  It is transmitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRSP/43, para. 34).

Add a new paragraph 1.5., to read:

"1.5.	It also applies to the installation of child restraint systems and ISOFIX child restraint systems designated for installation in vehicles of category M1, M2, M3 and N1. */"

Paragraph 8.3.5., amend to read:

"8.3.5.	In order to inform the vehicle user(s) of the provisions made for the transport of children, vehicles of categories M1, M2, M3 and N1 shall meet the information requirements of Annex 17.  Any vehicle of category M1 shall be equipped with ISOFIX positions, in accordance with the relevant prescriptions of Regulation No. 14.

The first……"

# - - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.