Proposal for draft Corrigendum 1 to Revision 5 to Regulation No. 37 (Filament lamps)

A.	PROPOSAL

Annex 1,

Sheet R5W/1, the table, change to read:

"…..

| Reference luminous flux at approximately 13.5 V: | White: 50 lm Red: 12 lm |
| --- | --- |

……"

B.	JUSTIFICATION

This is to correct a typographical error in the reference luminous flux specification for RR5W.  This error had occurred with the introduction of Revision 4 of Regulation No. 37.

- - - - -