| Transmitted by the expert from France | Informal document No. GRE-62-24 (62nd GRE, 6 -9 October 2009, agenda item 4(g)) |
| --- | --- |

Proposal for draft Corrigendum 1 to Supplement 4 to the 03 series of amendments of Regulation No. 48

(Installation of lighting and light-signalling devices)

A.	PROPOSAL

The modifications to the current text of Regulation No. 48 are marked in bold or strikethrough characters.

Annex 7, the title, amend to read:

"Annex 7

Indication of the downward inclination of the dipped beam headlamps cut-off referred to in paragraph 6.2.6.1.1. and downward inclination of the front fog lamp cut-off  referred to in paragraph 6.3.6.1.2. of this regulation

….."

B. 	JUSTIFICATION

Annex 7 of Regulation No. 48 has been modified by Supplement 4 to the 03 series of amendments to Regulation No. 48 in order to provide with the initial downward inclination value for front fog lamp as required in new paragraph 6.3.6.1.2 of Supplement 4, in addition to the same criteria linked to the dipped beam headlamp as required by the paragraph 6.2..6.1.1.

Supplement 4 to the 03 series of amendments to Regulation No. 48 modified the annex 7 which is providing now with the downward inclination values for dipped beam headlamps and front fog lamps but made a mistake by deleting the reference to dipped beam headlamps in the title of the annex.