| Transmitted by the expert from France | Informal document No. GRE-62-34 (62nd GRE, 6 -9 October 2009, agenda item 8) |
| --- | --- |

Proposal for draft Corrigendum 1 to the 03 series of amendments of Regulation No. 10

(Electromagnetic compatibility)

A. Proposal

The modifications are marked in bold or strikethrough characters.

Paragraph 8.3.1, amend to read

" 8.3.1.	When the conformity of a vehicle, component or ESA taken from the series is being verified, production shall be deemed to conform to the requirements of this Regulation in relation to broadband electromagnetic disturbances and narrowband electromagnetic disturbances if the levels measured do not exceed by more the 2 dB (25%) 4 dB (60 %) the reference limits prescribed in paragraphs 6.2.2.1., 6.2.2.2., 6.3.2.1. and 6.3.2.2. (as appropriate). "

B. Justification

R 10.03 prescriptions were taken from the directive 2009/19/EC. 2009/19/EC directive requires a relaxation of 4 dB for emissions levels for conformity of production see clause 7.3.1.

This document is to proposed to correct in R 10.03 the value of 2 dB  see clause 8.3.1 to align R 10.03 to directive 2009/19 EC  directive.

Directive 2009/19/EC

"7.3.1. If the conformity of a vehicle, component or STU taken from the series is being verified, production shall be deemed to conform to the requirements of this Directive in relation to broadband radiated emissions and narrowband radiated emissions if the levels measured do not exceed by more than 4 dB (60 %) the type approval limits prescribed in paragraphs 6.2.2.1, 6.2.2.2, 6.3.2.1, 6.3.2.2, 6.3.2.4, 6.5.2.1 and 6.6.2.1 (as appropriate)."

- - - - -