| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2010/26 18 December 2009 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

# One-hundred-and-fiftieth session

Geneva, 9-12 March 2010

Item 4.2.29 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 13 to Regulation No. 77

(Parking lamps)

Submitted by the Working Party on Lighting and Light-Signalling (/

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-second session.  It is based on informal document No. GRE-62-10, as reproduced in Annex IV to the report.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/62, para. 19).

Insert a new paragraph 6.3.3., to read:

"6.3.3.	A light source module shall be so designed that regardless of the use of tool(s), it shall not be mechanically interchangeable with any replaceable approved light source."

- - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.