|  | United Nations | ECE/TRANS/WP.29/2010/68 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 8 April 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fifty-first session

Geneva, 22 – 25 June 2010

Item 4.2.7 of the provisional agenda

1958 Agreement - Consideration of draft

amendments to existing Regulations

Proposal for Corrigendum 2 to the 03 series of amendments to Regulation No. 78 (Motorcycle braking)

Submitted by the Working Party on Brakes and Running Gear*

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its sixty-seventh session in order to correct Regulation No. 78 on Braking (category L vehicles). It is based on ECE/TRANS/WP.29/GRRF/2010/15, not amended (ECE/TRANS/WP.29/GRRF/67, para. 20). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Annex 3, paragraph 1.1.3., amend to read:

“1.1.3.		Measurement of PBC:

The PBC is measured as determined by the approval authority using either:

(a)	The American Society for Testing and Materials (ASTM) E1136 – 93 (Reapproved 2003) standard reference test tyre, in accordance with ASTM Method E1337-90 (Reapproved 2002), at a speed of 40 mph or

(b)	…”

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.