PROPOSAL FOR DRAFT CORRIGENDUM

TO SUPPLEMENT 4 OF THE 04 SERIES OF REGULATION NO.. 48

- PROPOSAL

The proposed corrigendum is shown in bold characters.

"2.10. 	The "apparent surface" for a defined direction of observation means, at the request of the manufacturer or his duly accredited representative, the orthogonal projection of:

either the boundary of the illuminating surface projected on the exterior surface of the lens;

or the light-emitting surface;

in a plane perpendicular to the direction of observation and tangential to the most exterior point of the lens.  Different examples of the application of apparent surface can be found in Annex 3 to this Regulation.

Only in the case of a light-signalling device producing variable luminous intensities, its apparent surface that may be variable as specified in paragraph 2.7.1.3 shall be considered under all conditions permitted by the variable intensity control, if applicable.”

- JUSTIFICATION

The text shown above in bold characters was inadvertently deleted during the drafting of the amendment proposed by GTB in GRE/2009/18 adopted at the 61st session and now in force as supplement 4 of the 04 series of Regulation No.48. This corrigendum is intended to reinstate this provision.