|  | United Nations | ECE/TRANS/WP.29/2011/97 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 29 July 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

155th session

Geneva, 15–18 November 2011

Item 4.6.3 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 38 to the 03 series of amendments to Regulation No. 37 (Filament lamps of power-driven vehicles and their trailers)

Submitted by the Working Party on Lighting and Light-Signalling*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-fifth session to phase out some light source categories from the Regulation. It is based on ECE/TRANS/WP.29/GRE/2011/18 and ECE/TRANS/WP.29/GRE/2011/18/Corr.1, as amended by Annex II to the report (ECE/TRANS/WP.29/GRE/65, para. 5). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraphs 8.3. and 8.4., amend to read:

"8.3.	No filament lamps of the categories or of the types within the categories listed below shall be used in lamps submitted for type approval after the period following the entry into force of the Supplements to 03 Series of amendment, as indicated for each category in the table of group 3 in Annex 1.

8.4.	However, Contracting Parties applying this Regulation may continue to grant approvals for lamps in which filament lamps of categories or of types within categories listed below are used, provided that these lamps are intended as replacement parts for installation on vehicles in use, for the period after entry into force of the Supplements to 03 Series of amendment as indicated in the table of group 3 in Annex 1."

Annex 1, the list of categories of filament lamps and their sheets, amend to read:

"....

Group 1

Without general restrictions:

| Category |  | Sheet number(s) |
| --- | --- | --- |
| H1 | *6 | H1/1 to 3 |
| H3 | *6 | H3/1 to 4 |
| H4 |  | H4/1 to 5 |
| H7 |  | H7/1 to 4 |
| H8 |  | H8/1 to 4 |
| H8B |  | H8/1 to 4 |
| H9 | *3 | H9/1 to 4 |
| H9B | *3 | H9/1 to 4 |
| H10 |  | H10/1 to 3 |
| H11 |  | H11/1 to 4 |
| H11B |  | H11/1 to 4 |
| H12 |  | H12/1 to 3 |
| H13 |  | H13/1 to 4 |
| H13A |  | H13/1 to 4 |
| H15 |  | H15/1 to 5 |
| H16 |  | H16/1 to 4 |
| H16B |  | H16/1 to 4 |
| H21W | *2 | H21W/1 to 2 |
| H27W/1 |  | H27W/1 to 3 |
| H27W/2 |  | H27W/1 to 3 |
| HB3 |  | HB3/1 to 4 |
| HB3A |  | HB3/1 to 4 |
| HB4 |  | HB4/1 to 4 |
| HB4A |  | HB4/1 to 4 |
| HIR1 | *3 | HIR1/1 to 3 |
| HIR2 |  | HIR2/1 to 3 |
| HS1 | *6 | HS1/1 to 5 |
| HS2 | *6 | HS2/1 to 3 |
| HS5 |  | HS5/1 to 4 |
| HS5A | *5 | HS5A/1 to 3 |
| HS6 | *4 | HS6/1 to 4 |
| PSX24W | *2 | P24W/1 to 3 |
| PSX26W | *2 | PSX26W1 to 3 |
| PX24W | *2 | P24W/1 to 3 |
| S2 | *6 | S1/S2/1 to 2 |

Group 2

Only for use in signalling lamps, cornering lamps, reversing lamps and rear registration plate lamps:

| Category |  | Sheet number(s) |  |
| --- | --- | --- | --- |
| C5W | *6 | C5W/1 |  |
| H6W |  | H6W/1 |  |
| H10W/1 |  | H10W/1 to 2 |  |
| HY6W |  | H6W/1 |  |
| HY10W |  | H10W/1 to 2 |  |
| HY21W |  | H21W/1 to 2 |  |
| P13W |  | P13W/1 to 3 |  |
| P21W | *6 | P21W/1 to 2 |  |
| P21/4W |  | P21/4W/1 | (P21/5W/2 to 3) |
| P21/5W | *6 | P21/5W/1 to 3 |  |
| P24W |  | P24W/1 to 3 |  |
| P27W |  | P27W/1 to 2 |  |
| P27/7W |  | P27/7W/1 to 3 |  |
| PR21W |  | PR21W/1 | (P21W/2) |
| PR21/4W |  | PR21/4W/1 | (P21/5W/2 to 3) |
| PR21/5W |  | PR21/5W/1 | (P21/5W/2 to 3) |
| PR27/7W |  | PR27/7W/1 | (P27/7W/2 to 3) |
| PS19W |  | P19W/1 to 3 |  |
| PS24W |  | P24W/1 to 3 |  |
| PSY19W |  | P19W/1 to 3 |  |
| PSY24W |  | P24W/1 to 3 |  |
| PW13W |  | P13W/1 to 3 |  |
| PW16W |  | PC16W/1 to 3 |  |
| PWR16W |  | PC16W/1 to 3 |  |
| PWY16W |  | PC16W/1 to 3 |  |
| PW19W |  | P19W/1 to 3 |  |
| PWR19W |  | P19W/1 to 3 |  |
| PWY19W |  | P19W/1 to 3 |  |
| PW24W |  | P24W/1 to 3 |  |
| PWR24W |  | P24W/1 to 3 |  |
| PWY24W |  | P24W/1 to 3 |  |
| PY21W |  | PY21W/1 | (P21W/2) |
| PY24W |  | P24W/1 to 3 |  |
| PY27/7W |  | PY27/7W/1 | (P27/7W/2 to 3) |
| R5W | *6 | R5W/1 |  |
| R10W | *6 | R10W/1 |  |
| RR5W | *6 | R5W/1 |  |
| RR10W | *6 | R10W/1 |  |
| RY10W | *6 | R10W/1 |  |
| T1.4W |  | T1.4W/1 |  |
| T4W | *6 | T4W/1 |  |
| W2.3W |  | W2.3W/1 |  |
| W3W | *6 | W3W/1 |  |
| W5W | *6 | W5W/1 |  |
| W10W | *6 | W10W/1 |  |
| W15/5W |  | W15/5W/1 to 3 |  |
| W16W |  | W16W/1 |  |
| W21W |  | W21W/1 to 2 |  |
| W21/5W |  | W21/5W/1 to 3 |  |
| WP21W |  | WP21W/1 to 2 |  |
| WPY21W |  | WP21W/1 to 2 |  |
| WR5W |  | W5W/1 |  |
| WR21/5W |  | WR21/5W/1 | (W21/5W/2 to 3) |
| WY2.3W |  | WY2.3W/1 |  |
| WY5W |  | W5W/1 |  |
| WY10W | *6 | W10W/1 |  |
| WY16W |  | W16W/1 |  |
| WY21W |  | WY21W/1 to 2 |  |

Group 3

For replacement purposes only:

|  |  |  | As specified by transitional provisions in paragraph 8.3 | As specified by transitional provisions in paragraph 8.4 |
| --- | --- | --- | --- | --- |
| Category |  | Sheet number(s) | Supplement | Period | Supplement | Period |
| C5W | *7, *8 | C5W/1 | 38 | 12 months | 38 | unlimited |
| C21W | *8 | C21W/1 to 2 | 28 | 12 months | 28 | unlimited |
| H1 | *7 | H1/1 to 3 | 38 | 12 months | 38 | unlimited |
| H3 | *7 | H3/1 to 4 | 38 | 12 months | 38 | unlimited |
| H14 |  | H14/1 to 4 | 38 | 12 months | 38 | unlimited |
| HS1 | *7 | HS1/1 to 5 | 38 | 12 months | 38 | unlimited |
| HS2 | *7 | HS2/1 to 3 | 38 | 12 months | 38 | unlimited |
| P19W | *8 | P19W/1 to 3 | 37 | 60 months | 37 | unlimited |
| P21W | *7, *8 | P21W/1 to 2 | 38 | 12 months | 38 | unlimited |
| P21/5W | *7, *8 | P21/5W/1 to 3 | 38 | 12 months | 38 | unlimited |
| PC16W | *8 | PC16W/1 to 3 | 37 | 60 months | 37 | unlimited |
| PCR16W | *8 | PC16W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PCY16W | *8 | PC16W/1 to 3 | 37 | 60 months | 37 | unlimited |
| PR19W | *8 | P19W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PR24W | *8 | P24W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PSR19W | *8 | P19W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PSR24W | *8 | P24W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PY19W | *8 | P19W/1 to 3 | 37 | 60 months | 37 | unlimited |
| R2 |  | R2/1 to 3 | 28 | 12 months | 28 | unlimited |
| R5W | *7, *8 | R5W/1 | 38 | 12 months | 38 | unlimited |
| R10W | *7, *8 | R10W/1 | 38 | 12 months | 38 | unlimited |
| RR5W | *7, *8 | R5W/1 | 38 | 12 months | 38 | unlimited |
| RR10W | *7, *8 | R10W/1 | 38 | 12 months | 38 | unlimited |
| RY10W | *7, *8 | R10W/1 | 38 | 12 months | 38 | unlimited |
| S1 |  | S1/S2/1 to 2 | 28 | 12 months | 28 | unlimited |
| S2 | *7 | S1/S2/1 to 2 | 38 | 12 months | 38 | unlimited |
| S3 |  | S3/1 | 38 | 12 months | 38 | unlimited |
| T4W | *7, *8 | T4W/1 | 38 | 12 months | 38 | unlimited |
| W3W | *7, *8 | W3W/1 | 38 | 12 months | 38 | unlimited |
| W5W | *7, *8 | W5W/1 | 38 | 12 months | 38 | unlimited |
| W10W | *7, *8 | W10W/1 | 38 | 12 months | 38 | unlimited |
| WY10W | *7, *8 | W10W/1 | 38 | 12 months | 38 | unlimited |

*	Tables, Electrical and Photometric characteristics:

Voltage is expressed in V;

Wattage is expressed in W;

Luminous flux is expressed in lm.

In a case that for a category of filament lamp more than one value of reference luminous flux is specified, the value at approximately 12 V for approval of a lighting device and 13.5 V for approval of a light-signalling device shall be applied unless otherwise specified by the regulation used for the approval of the device.

*2	Not for use in passing beam headlamps.

*3	Not for use in front fog lamps marked "B" as defined in Regulation No. 19.

*4	Not for use in Regulation No. 112 headlamps.

*5	Not for use in headlamps other than Regulation No. 113 class C headlamps

*6	All types except from 6 V type

*7	6 V types only

*8	Only for use in signalling lamps, cornering lamps, reversing lamps and rear registration plate lamps."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208/, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.