|  | United Nations | ECE/TRANS/WP.29/GRE/2013/5 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 25 January 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-ninth session

Geneva, 8-11 April 2013

Item 5(f) of the provisional agenda
Collective amendments — Regulations Nos. 5 and 31

Proposal for Collective Amendments to Regulations No. 5 (Sealed beam headlamps) and Regulation No. 31 (Headlamps (halogen sealed beam (HSB)))

Submitted by the expert from the International Automotive Lighting and Light Signalling Expert Group (GTB) *

The text reproduced below was prepared by the expert from the International Automotive Lighting and Light Signalling Expert Group (GTB) to amend the transitional provisions to cease granting new type approvals for the "Sealed Beam" headlamps and to correct the title of UN Regulation No. 31. The modifications to the existing text of the Regulation are shown in "track changes" mode.

I.	Proposal

A.	Proposal for the 03 series of amendments to Regulation No. 5

Paragraph 15., amend to read:

"15.	TRANSITIONAL PROVISIONS

15.1.	As from [twelve] months after the official date of entry into force of the 03 Series of this Regulation, Contracting Parties applying this Regulation shall cease to grant ECE approvals according to this Regulation.

15.2.	Contracting Parties applying this Regulation shall not refuse to grant extensions of approval to this and any previous series of amendments of this Regulation.

15.3.	Existing approvals granted before the official date of entry into force of the 03 Series of this Regulation and all extensions of approvals, including those to a preceding series of amendments to this Regulation granted subsequently, shall remain valid indefinitely.

15.4.	Contracting Parties applying this Regulation shall continue to issue approvals for headlamps on the basis of this and any previous series of amendments to this Regulation, provided that the headlamps are intended as replacements for fitting to vehicles in use.

15.5.	Contracting Parties applying this Regulation shall continue to allow fitting of a headlamp approved to this Regulation on a vehicle or vehicle type.

15.6.	Contracting Parties applying this Regulation shall continue to allow fitting or use on a vehicle in use of a headlamp approved to this Regulation as amended by any previous series of amendments, provided that the headlamp is intended for replacement."

B.	Proposal for the 03 series of amendments to Regulation No. 31

The title of the Regulation, amend to read:

"UNIFORM PROVISIONS CONCERNING THE APPROVAL OF POWER-DRIVEN VEHICLE'S HALOGEN SEALED-BEAM HEADLAMPS (HSB) EMITTING A EUROPEAN ASYMMETRICAL PASSING BEAM OR A DRIVING BEAM OR BOTH"

Paragraph 15., amend to read:

"15.1.	As from [twelve] months after the official date of entry into force of the 03 Series of this Regulation, Contracting Parties applying this Regulation shall cease to grant ECE approvals according to this Regulation.

15.2.	Contracting Parties applying this Regulation shall not refuse to grant extensions of approval to this and any previous series of amendments of this Regulation.

15.3.	Existing approvals granted before the official date of entry into force of the 03 Series of this Regulation and all extensions of approvals, including those to a preceding series of amendments to this Regulation granted subsequently, shall remain valid indefinitely.

15.4.	Contracting Parties applying this Regulation shall continue to issue approvals for headlamps on the basis of this and any previous series of amendments to this Regulation, provided that the headlamps are intended as replacements for fitting to vehicles in use.

15.5.	Contracting Parties applying this Regulation shall continue to allow fitting of a headlamp approved to this Regulation on a vehicle or vehicle type.

15.6.	Contracting Parties applying this Regulation shall continue to allow fitting or use on a vehicle in use of a headlamp approved to this Regulation as amended by any previous series of amendments, provided that the headlamp is intended for replacement."

II.	Justification

1.	The title of UN Regulation No. 31 was amended by a proposal from the European Commission in 2005 (TRANS/WP.29/GRE/2005/27) deleting the abbreviation ("HSB") as well as the word "Halogen". The motivation for the deletion of the reference to "Halogen" and "HSB" is not clear but it results in the loss of the differentiation between UN Regulations Nos. 5 and 31. As the text of UN Regulation No. 31 consistently refers to "HSB" (see paras. 2.1., 2.4., 3.1.1., 4.1. etc.), and the text of UN Regulation No. 5 consistently refers to "SB", it would appear logical to revert to the original title of UN Regulation No. 31.

2.	In addition to the above comments, GRE at its 68th session, basically agreed with the proposal of GTB to "freeze" the "Sealed Beam" Regulations, to prevent new type approvals being granted, as was done in the case of UN Regulations Nos. 2, 8 and 20. The GTB experts are of the opinion that regulations permitting type approval of the outdated "sealed beam headlamp" technologies are no longer appropriate.

3.	It is proposed to introduce a new series of amendments for both Regulations 5 and 31 with transitional provisions that would cease to allow new type approvals to be granted. The transitional period of 12 months has been left for the decision of GRE.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106, ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.