Proposal for the correct adoption of Supplement 3 to the 03 Series into Regulation 19-Revision 6

I.	Proposal

The photometric table in paragraph 6.4.3.of Revision 6, to read:

| Designated lines or zones | Vertical position* above h + below h - | Horizontal position* left of v: - right of v: + | Luminous intensity (in cd) | To comply |
| --- | --- | --- | --- | --- |
| Line 6*** | -2.5° | from 5° inwards to 10° outwards -10° to +10° | 2,700 min | All line |
| Line 7*** | -6.0° | from 5° inwards to 10° outwards -10° to +10° | < 50 per cent of max. on line 6 | All line |

II.		Justification

The proposal for Corrigendum 6 to the 03 series of Regulation No.19 was originated in GRE with informal document GRE 65-27, prepared by the expert from Germany. It was adopted by WP29 at its 155th session (ECE/TRANS/WP.29/2011/130) as Supplement 3 to the 03 series of amendments to Regulation No. 19.

Whilst the amendment introduced as Supplement 3 to the 03 series will automatically apply to the 04 series currently in force, in this instance it is necessary to ensure that the changes are applied correctly in the photometric table of paragraph 6.4.3 because the photometric values differ between the 03 and the 04 series.

Note: Comparison of the 03 and 04 series photometric tables in paragraph 6.4.3.

The amendment in Supplement 3 to the 03 series reads:

| Line 6 *** | - 2.5° | - 10° to + 10° | 2,000 min | All line |
| --- | --- | --- | --- | --- |
| Line 7*** | - 6.0° | - 10° to + 10° | < 50 per cent of max. on line 6 | All line |

The corresponding lines in the table of the Revision 6 should read:

| Line 6*** | -2.5° | from 5° inwards to 10° outwards- -10° to +10° | 2,700 min | All line |
| --- | --- | --- | --- | --- |
| Line 7*** | -6.0° | from 5° inwards to 10° outwards- - 10° to +10° | < 50 per cent of max. on line 6 | All line |

As Supplement 3 to the 03 series of amendments to Regulation No. 19 (ECE/TRANS/WP.29/2011/130) was adopted by WP29 in November 2011 it can be expected to enter into force in July 2012. It is therefore important to ensure that the 03 and 04 series of amendments are correctly coordinated at this time. Presumably this will be best accomplished by a corrigendum to the 04 series that is submitted by the secretariat and adopted by WP29 at its 157th session in June 2012.