| Transmitted by the expert from GTB | Informal Document No. GRE-67-18 (67th GRE, 26–29 March 2012) agenda item 5(c) |
| --- | --- |

Proposal for Addendum to ECE/TRANS/WP.29/GRE/2012/7

I.	Proposal

Proposal for Supplement 8 to the 02 series of amendments of Regulation 31

Paragraph 2.4., amend to read:

“2.4.	"HSB units of different types" means units which differ in such essential respects as:

2.4.1.	the trade name or mark;

2.4.2.	the characteristics of the optical system;

2.4.3.	the inclusion or elimination of components capable of altering the optical effects by reflection, refraction, absorption and/or deformation during operation; the fitting or elimination of filters intended solely to change the colour of the beam but not its light distribution does not constitute a change of type;

2.4.4.	the rated voltage;

2.4.5.	the shape of the filament or filaments;

2.4.6.	the kind of beam produced (passing beam, driving beam or both);

2.4.7.	the materials constituting the lens and coating, if any.”

II.		Justification

During the preparation of the proposal in ECE/TRANS/WP.29/GRE/2012/7) the corresponding amendment to Regulation No. 31 was unintentionally omitted. This addendum completes the collective amendment.