|  | United Nations | ECE/TRANS/WP.29/2013/18 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 21 December 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

159th session

Geneva, 12-15 March 2013

Item 4.11.5 of the provisional agenda

1958 Agreement – Consideration of draft corrigenda
to existing Regulations submitted by the secretariat

Proposal for Corrigendum 1 to Supplement 13 to the 01 series of amendments to Regulation No. 53 (Installation of lighting on L3 vehicles)

Note by the secretariat*

The text reproduced below was prepared by the secretariat to reinsert a provision for the colour of Daytime Running Lamp (DRL) deleted by mistake when the proposal for Supplement 13 to the 01 series of amendments to the Regulation was prepared by the secretariat. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraph 5.13., correct to read (reinsertion of the last line):

"5.13. 		Colours of the lights

The colours of the lights referred to in this Regulation shall be as follows:

driving beam headlamp: 			white

passing beam headlamp:			white

direction-indicator lamp: 			amber

stop lamp: 					red

rear-registration plate lamp: 		white

front position lamp: 				white or amber

rear position lamp: 				red

rear retro-reflector, non-triangular: 		red

side retro-reflector, non-triangular: 	amber at the front

amber or red at the rear

vehicle-hazard warning signal: 		amber

front fog lamp : 				white or selective yellow

rear fog lamp : 				red

Daytime running lamp			white."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.