|  | Nations Unies | ECE/TRANS/WP.29/2013/121 |
| --- | --- | --- |
|  | Conseil économique et social | Distr. générale 26 juillet 2013 Français Original: anglais |

Commission économique pour l’Europe

Comité des transports intérieurs

Forum mondial de l’harmonisation
des Règlements concernant les véhicules

161e session

Genève, 12-15 novembre 2013

Point 14.1 de l’ordre du jour provisoire

Examen et vote par l’AC.3 concernant des projets de Règlements
techniques mondiaux ou des projets d’amendements
à des Règlements techniques mondiaux existants

Rapport final sur la proposition de nouveau 
Règlement technique mondial sur les essais 
de choc latéral contre un poteau

Communication du Groupe de travail de la sécurité passive*

Le texte ci-après, adopté par le Groupe de travail de la sécurité passive (GRSP) à sa cinquante-troisième session, vise à introduire un nouveau Règlement technique mondial (RTM) sur les essais de choc latéral contre un poteau. Il est fondé sur un document distribué sans cote (GRSP-53-04-Rev.1), tel qu’il est reproduit à l’annexe II du rapport (ECE/TRANS/WP.29/GRSP/53, par. 11). Il est soumis au Forum mondial de l’harmonisation des Règlements concernant les véhicules (WP.29) et au Comité exécutif de l’Accord de 1998 (AC.3) aux fins d’examen et de mise aux voix à leurs sessions de novembre 2013 en même temps que le projet de RTM (ECE/TRANS/WP.29/2013/120) et la proposition d’élaboration du projet de RTM contenu dans le document ECE/TRANS/WP.29/AC.3/28.

Rapport final du groupe de travail informel 
sur un Règlement technique mondial sur les essais
de choc latéral contre un poteau

A.	Introduction

Le but du présent rapport est de compléter les informations de procédure relatives à l’élaboration du RTM contenues dans la première partie (Exposé des motifs techniques et justification du Règlement) du RTM et de fournir des détails supplémentaires concernant le groupe de travail informel.

Pour obtenir des informations sur l’argumentation technique justifiant l’élaboration de ce Règlement technique mondial, veuillez consulter la première partie du RTM.

B.	Historique

Lors de la 150e session du Forum mondial de l’harmonisation des Règlements concernant les véhicules (WP.29), en mars 2010, le représentant de l’Australie a soumis le document informel (WP.29-150-11) proposant l’élaboration d’un Règlement technique mondial (RTM) sur les essais de choc latéral contre un poteau. Il s’articule autour des cinq arguments principaux suivants:

a)	Un grand nombre de décès sont dus à un choc latéral contre des objets étroits, principalement des poteaux télégraphiques, des poteaux indicateurs ou des arbres, mais aussi contre d’autres objets, tant en Australie que dans d’autres pays;

b)	Les modalités des essais sont très différentes selon qu’il s’agit d’essais de choc latéral contre un poteau ou d’autres essais de choc latéral aussi bien aux fins de la réglementation que de l’établissement de normes non contraignantes;

c)	La grande variété des modèles de mannequins utilisés dans les essais de choc et des appréciations concernant leurs caractéristiques de biofidélité fait que d’aucuns s’interrogent sur leur utilité pour l’évaluation des blessures;

d)	Grâce à son degré de biofidélité élevé le mannequin WorldSID homme du 50e centile a permis d’améliorer la fiabilité des essais de choc latéral et, avec l’élaboration d’un RTM sur les essais de choc latéral contre un poteau, d’améliorer la sécurité des usagers mais aussi de faire faire des économies aux consommateurs et aux constructeurs; et

e)	Une norme unique d’essais de choc latéral contre un poteau devrait être bénéfique pour les chocs latéraux en général en rendant possible une meilleure protection de la tête.

Le Comité exécutif de l’Accord de 1998 (AC.3) a chargé le secrétariat du WP.29 de faire distribuer le document WP.29-150-11 sous une cote officielle, aux fins d’examen et de vote à sa session de juin 2010. Il a été décidé de transmettre le document WP.29-150-11 au Groupe de travail de la sécurité passive (GRSP) pour qu’il l’examine à sa session de mai 2010 et évalue la nécessité de créer un groupe de travail informel.

À sa quarante-septième session, en mai 2010, le GRSP a examiné une proposition officielle présentée par l’expert de l’Australie (ECE/TRANS/WP.29/2010/81), ainsi qu’un nouveau document sans cote (GRSP-47-28) contenant une proposition de liste de travaux (qui est ensuite devenue un mandat) et entériné la création d’un groupe de travail informel présidé par l’Australie, sous réserve de l’acceptation par l’AC.3.

Lors de la 151e session du WP.29, en juin 2010, l’AC.3 a examiné une proposition officielle soumise par le représentant de l’Australie et a accepté l’idée d’élaborer un RTM et de créer le groupe de travail informel. L’AC.3 a en outre décidé que les principales tâches du groupe de travail informel seraient les suivantes:

a)	Confirmer la nécessité, du point de vue de la sécurité, d’élaborer un RTM compte tenu du nombre croissant de véhicules équipés d’un système de stabilité électronique; et

b)	Évaluer dans le même temps les différentes normes potentielles en matière d’essais de choc à utiliser dans le futur RTM. La proposition a été incluse dans la liste des propositions d’élaboration de RTM, adoptée par l’AC.3 (ECE/TRANS/ WP.29/AC.3/28).

À la 154e session du WP.29, en juin 2011, l’AC.3 a adopté le mandat du groupe de travail informel ainsi que son premier rapport d’activité (ECE/TRANS/WP.29/2011/87).

À la 157e session du WP.29, en juin 2012, l’AC.3 a adopté le deuxième rapport d’activité du groupe de travail informel, ainsi qu’une modification de son mandat, afin de prévoir que, dans un deuxième temps, le RTM inclue le mannequin WorldSID femme du 5e centile (ECE/TRANS/WP.29/2012/59). Le mandat modifié figure dans l’annexe 1.

À la cinquante et unième session du GRSP, en mai 2012, le groupe de travail informel avait soumis l’avant-projet de la partie II du RTM (GRSP-51-16).

À la 158e session du WP.29, en novembre 2012, l’AC.3 a décidé que le mandat du groupe de travail informel durerait pour la première phase jusqu’en mars 2014, partant du principe qu’un projet officiel de RTM serait examiné par l’AC.3 en novembre 2012, mais que des retards étaient possibles. Il a aussi été relevé qu’en raison de l’incertitude du calendrier en ce qui concerne la validation du mannequin WorldSID femme du 5e centile une proposition de délai pour la deuxième phase serait avancée séparément.

À la cinquante-deuxième session du GRSP, en décembre 2012, le groupe de travail informel a soumis l’avant-projet de la partie I et un projet plus élaboré de partie II (GRSP-52-07).

À la cinquante-troisième session du GRSP, en mai 2013, le groupe de travail informel a soumis la proposition de Règlement technique mondial sur les essais de choc latéral contre un poteau (ECE/TRANS/WP.29/GRSP/2013/7) et la proposition d’amendements au document ECE/TRANS/WP.29/GRSP/2013/7 (GRSP-53-05).

Le GRSP a accepté l’essentiel des amendements proposés au document ECE/TRANS/WP.29/GRSP/2013/7 contenus dans le document informel GRSP-53-05 et il a apporté un certain nombre de modifications supplémentaires au texte. Elles apparaissent clairement mises en évidence dans le document GRSP-53-23. Le GRSP a adopté le document ECE/TRANS/WP.29/GRSP/2013/7 tel que modifié par le document GRSP-52-23, afin qu’il puisse être mis à disposition en tant que document de travail pour examen par l’AC.3 en novembre 2013.

Détail des activités du groupe de travail informel:

Le groupe de travail informel a tenu les réunions suivantes:

a)	1e réunion, Bonn, 16-18 novembre 2010;

b)	2e réunion, Bruxelles, 3 et 4 mars 2011;

c)	3e réunion, Washington, 9 juin 2011;

d)	4e réunion, Séoul, 27 et 28 octobre 2011;

e)	5e réunion, Londres, 22 et 23 mars 2012;

f)	6e réunion, Munich, 20 et 21 juin 2012;

g)	7e réunion, Washington, 20 et 21 septembre 2012;

h)	8e réunion, Paris, 20 et 21 novembre 2012.

Le groupe de travail informel a également tenu une séance de rédaction par l’intermédiaire du système Webex le 7 février 2013.

Ont participé à ces réunions des représentants des organisations et des pays suivants: Allemagne, Australie, Canada, Chine, Commission européenne, États-Unis d’Amérique, France, Japon, Pays-Bas, République de Corée, Royaume-Uni et Organisation internationale des constructeurs d’automobiles (OICA).

Un certain nombre d’autres organisations, notamment des organismes de recherche, ont assisté à plusieurs réunions et des documents ont été amplement diffusés.

Les réunions étaient présidées par M. Robert Hogan, tandis que le secrétariat et le support technique étaient assurés par M. Thomas Belcher et M. Mark Terrell, du Département australien de l’infrastructure et des transports.

Le groupe de travail informel sur le RTM a collaboré étroitement avec le groupe de travail informel sur l’harmonisation des mannequins pour essai de choc latéral (groupe d’étude WorldSID), qui se réunissait en général immédiatement avant le groupe sur le RTM, ce qui permettait aux participants d’assister aux deux réunions.

De nombreux documents ont été cités ou élaborés par le groupe de travail informel, notamment des procès-verbaux et des exposés qui, avec les documents soumis par le GRSP, fournissent une chronologie de l’élaboration du RTM. Ces documents sont énumérés dans l’annexe 2 et ils peuvent être consultés sur le site Web de la CEE à l’adresse: https://www2.unece.org/wiki/pages/viewpage.action?pageId=3178630.

Annexe 1

Mandat révisé

Le groupe informel est principalement chargé des tâches suivantes:

a)	Examiner les travaux de recherche existants, notamment les résultats d’essais de choc, ainsi que la littérature;

b)	Coordonner ses résultats avec ceux des réunions du groupe informel du GRSP sur le mannequin WorldSID;

c)	Évaluer les besoins en matière de sécurité, et notamment analyser l’état actuel des décès et des blessures provoqués par des chocs latéraux contre des poteaux, par d’autres chocs latéraux ou par le renversement de véhicules, en tenant compte d’évolutions positives déjà acquises ou probables, comme l’introduction des systèmes de contrôle de stabilité et cibler les catégories de véhicules à prendre en considération;

d)	Examiner les procédures d’essai possibles;

e)	Étudier les variations possibles dans les procédures d’essai concurrentes;

f)	Mettre au point des contre-mesures sur la base de procédures d’essai présélectionnées;

g)	Calculer jusqu’à quel point ces contre-mesures seraient susceptibles d’atténuer la gravité des accidents;

h)	Procéder à l’analyse coûts-avantages des procédures d’essai présélectionnées (en incluant les données provenant d’un large éventail de pays, car les avantages peuvent varier considérablement d’un pays à l’autre);

i)	Évaluer les possibles accroissements en termes de coûts et d’avantages résultant, par exemple, d’essais portant sur des individus plus petits (femme du 5e centile) et les occupants d’un siège du côté non soumis au choc ou d’un siège arrière;

j)	Sélectionner une procédure d’essai préférée;

k)	Préparer un projet de RTM − phase 1 (mannequin WorldSID homme du 50e centile) pour examen par le GRSP puis par le WP.29; et

l)	Préparer un projet de RTM − phase 2 (mannequin WorldSID femme du 5e centile) pour examen par le GRSP puis par le WP.29.

Annexe 2

Documents des réunions du groupe de travail informel

RD-01	National Highway Traffic Safety Administration (NHTSA): 49 CFR Parts 571 and 585 Federal Motor Vehicle Safety Standards; Occupant Protection in Interior Impact; Side Impact Protection; Fuel System Integrity; Electric-Powered Vehicles: Electrolyte Spillage and Electrical Shock Protection; Side Impact Phase-In Reporting Requirements; Final Rule (2007)

RD-02	NHTSA (Office of Regulatory Analysis and Evaluation, National Centre for Statistics and Analysis): FMVSS No. 214 Amending Side Impact Dynamic Test: Adding Oblique Pole Test (2007)

RD-03	NHTSA & Abacus Technology Corporation: NHTSA Side Impact Research: Motivation for Upgraded Test Procedures

RD-04	NHTSA: 49 CFR Parts 571 and 598 Federal Motor Vehicle Safety Standards; Side Impact Protection; Side Impact Phase-In Reporting Requirements; Proposed Rule (2004)

RD-05	NHTSA: 49 CFR Parts 571 and 585 [Docket No. NHTSA–2008–0104] RIN 2127–AK27 Federal Motor Vehicle Safety Standards; Occupant Protection in Interior Impact; Side Impact Protection; Side Impact Phase-In Reporting Requirements (2008)

PSI-01-01	Draft Agenda for the First Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-01-02	Request for Country Data

PSI-01-03	Pole Definition

PSI-01-04	Summary of Existing Crash Test and Simulation Data

PSI-01-05	GRSP Informal Group on a Pole Side Impact GTR (WP.29 and GRSP Decisions, Draft Procedures and Terms of Reference)

PSI-01-06	Agenda for the first meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-01-07	Australian Department of Infrastructure and Transport: Pole Side Impact gtr: Assessment of Safety Need: Initial Data Collection

PSI-01-08	German Federal Highway Research Institute (BASt): Influence of Vehicle Stability Control on Accidents on Rural Roads – GRSP Informal Group on a Pole Side Impact GTR

PSI-01-09	Australian Department of Infrastructure and Transport & Monash University Accident Research Centre (MUARC): Evaluating Vehicle Technologies – Electronic Stability Control Using Australian Used Car Safety Ratings Data

PSI-01-10	NHTSA: US Side Impact Pole Test – Federal Motor Vehicle Safety Standard No. 214

PSI-01-11	European Enhanced Vehicle-safety Committee (EEVC) Working Group 13 & Working Group 21: Accident Data: Side Impacts with Poles

PSI-01-12	Australian Department of Infrastructure and Transport: Summary of available test data

PSI-01-13	Australian Department of Infrastructure and Transport: Summary of current pole tests

PSI-01-14	Transport Canada: Pole Test Comparison of the WorldSID IRTRACC, WorldSID Rib-Eye & ES-2re

PSI-01-15	Australian Department of Infrastructure and Transport: Australian Pole Side Impact Research 2010 – A summary of recent oblique, perpendicular and offset perpendicular pole side impact research with WorldSID 50th

PSI-01-16	NHTSA: Calculating Benefits for Oblique Pole Side Impact Rulemaking

PSI-01-17	EEVC Working Group 13 & Working Group 21: Cost/Benefit of Side Impact Test Procedures

PSI-01-18	Transport Canada: WorldSID Positioning – Sub-Committee Update

PSI-02-01	Draft Agenda for the 2nd Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-02-02	First Progress Report of the Informal Group on a Pole Side Impact (PSI) GTR

PSI-02-03	Minutes of the First Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-02-04	Agenda for the 2nd meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-02-05	NHTSA: FMVSS No. 226 – Ejection Mitigation Final Rule

PSI-02-06	Australian Department of Infrastructure and Transport: Pole Side Impact GTR: Assessment of Safety Need: Updated Data Collection

PSI-02-07	Renault & PSA Peugeot Citroen: Pole Side Impact Accident Data – France National & LAB Data

PSI-02-08	Australian Department of Infrastructure and Transport: Application/Scope of PSI GTR (draft for discussion)

PSI-02-09	APROSYS: Car to Pole Side Impact Activities

PSI-02-10	NHTSA: WorldSID Crash Testing

PSI-02-11	NHTSA: Discussion of Injuries in Pole Side Impact Crashes – NHTSA’s Motivation for Upgrading the Side Impact Test Procedures & Benefit Analysis

PSI-02-12	BASt: Accident Data: Side Impacts with Poles – Informal Group on a Pole Side Impact GTR (PSI)

PSI-02-13	Australian Department of Infrastructure and Transport: Analysis of Vehicle Structural Deformation in Oblique, Perpendicular, and Offset Perpendicular Pole Side Impact

PSI-02-14	NHTSA: Real World Need for Oblique Test

PSI-02-15	ISO/WG6 & ACEA-TFD: Update on the WorldSID Injury Risk Curves

PSI-02-16	Australian Department of Infrastructure and Transport: Fatalities and Serious Injuries in Side Impact Crashes by Age – Victoria, Australia, 2000-2009

PSI-02-17	University of Michigan Transportation Research Institute: Effects of Occupant Age on AIS 3+ Injury Outcome Determined from Analyses of Fused NASS/CIREN Data

PSI-02-18	BMW Group: Side Pole Impact Accidents and Vehicle Testing

PSI-02-19	Australian Department of Infrastructure and Transport: Research Proposal – Quantitative analysis of Side Impact injuries, and effectiveness of existing countermeasures; Extension of existing work on side airbag effectiveness

PSI-03-01	Agenda for the 3rd Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-03-02	Minutes of the Second Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-03-03	Australian Department of Infrastructure and Transport & Transport Canada: Joint Australian and Canadian Pole Side Impact Research

PSI-03-04	Australian Department of Infrastructure and Transport: Pole Side Impact GTR: Assessment of Safety Need: Updated Data Collection

PSI-03-05	Australian Department of Infrastructure and Transport: Fatalities and Serious Injuries in Side Impact Crashes by Impact Type, Occupant Age and Year of Vehicle Manufacture, Victoria, Australia, 1999-2010

PSI-03-06	NHTSA: Incremental Benefits Perpendicular to Oblique Configuration

PSI-03-07	MUARC: Data Analysis to Investigate the Injury Profile of Near-Side, Side Impact Crashes: a Comparison of Injury Risk between Pole and Vehicle-Vehicle Impacts

PSI-03-08	Australian Department of Infrastructure and Transport: Scope of the GTR (draft for discussion)

PSI-03-09	Australian Department of Infrastructure and Transport: Options for the 5th Female

PSI-03-10	BASt: Accident Data: Side Impacts with Poles

PSI-03-11	BMW Group: WorldSID 50M – Injury Criteria

PSI-03-12	NHTSA: Repeatability of Oblique Test Configuration

PSI-04-01	Agenda for the 4th Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-04-02	Minutes of the Third Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-04-03	Australian Department of Infrastructure and Transport: Joint Australian and Canadian Pole Side Impact Research

PSI-04-04	French Technical Union for the Automobile, Motorcycle and Cycle Industries (UTAC): 4th Meeting of the GRSP Informal Group on Pole Side Impact GTR

PSI-04-05	Australian Department of Infrastructure and Transport: Safety Need – High Level Figures

PSI-04-06	Australian Department of Infrastructure and Transport: GTR Scope – N1 Occupant Fatalities in Australia

PSI-04-07	Australian Department of Infrastructure and Transport: Options for Addressing Gap in Readiness between WorldSID Male 50th and WorldSID Female 5th in Drafting the Pole Side Impact GTR

PSI-04-08	Australian Department of Infrastructure and Transport: Analysis of Australian National Crash In-Depth Study (ANCIS) Pole Side Impact Cases by Angle of Impact

PSI-04-09	NHTSA: Exclusions (in FMVSS 214)

PSI-04-10	OICA: Scope of GTR – Pole Side Impact – Commercial Vehicle Use and Data

PSI-04-11	JASIC/Japan: Japanese Proposal and Research Plan

PSI-04-12	Australian Department of Infrastructure and Transport: Draft Outline of Preamble of the gtr

PSI-04-13	Australian Department of Infrastructure and Transport: Draft Text of the Regulation of the gtr (NB a revised draft of this text was circulated to PSI Informal Group members on 4 November 2011 as a working document)

PSI-05-01	Agenda for the 5th Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-05-02	Minutes of the Fourth Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-05-03	MUARC: Analysis of In-depth and Mass Crash Data to Inform the Development of the Pole Side Impact Global Technical Regulation

PSI-05-04	BASt: Pole Side Impact Accidents in Germany

PSI-05-05	Australian Department of Infrastructure and Transport & Transport Canada: Joint Australian and Canadian Pole Side Impact Research

PSI-05-06	JASIC/Japan: Research TEST Result & Japanese Proposal

PSI-05-07	OICA: Pole Side Impact Protection – Cost Data – Based on Studies from EEVC and NHTSA

PSI-05-08	Australian Department of Infrastructure and Transport: Safety Need – High Level Figures

PSI-05-09	OICA: Scope of GTR – Pole Side Impact – Exemption of Commercial Vehicles

PSI-05-10	Australian Department of Infrastructure and Transport: The Importance of Pole Side Impact Alignment Accuracy

PSI-06-01	Agenda for the 6th Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-06-02	Minutes of the Fifth Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-06-03	MUARC: Further Injury Risk Analysis and the Cost-effectiveness of Enhanced Side Impact Protection in the Form of a GTR for PSI Crashes

PSI-06-04	Australian Department of Infrastructure and Transport & Transport Canada: Joint Australian and Canadian Pole Side Impact Research

PSI-06-05	UTAC: Pole Side Impact Test on European Berline

PSI-06-06	Australian Department of Infrastructure and Transport: Safety Need – High Level Figures

PSI-06-07	Australian Department of Infrastructure and Transport: Category 2 Vehicles: Australian Sales and Safety Need Data

PSI-06-08	ISO WorldSID 50th Task Group: Update to GTR Pole Side Impact

PSI-06-09	NHTSA: WorldSID 50th TEG: Status Report

PSI-06-10	Medical College of Wisconsin: Preliminary Analysis of Shoulder Traumas from the CIREN Database

PSI-06-11	Audi: Occupant Loading in Pole Side Impact

PSI-06-12	NHTSA: Pole Side Impact Vehicle Tests: WorldSID Dummy Data

PSI-06-13	Australian Department of Infrastructure and Transport & Transport Canada: Summary of Rib Deflection Responses

PSI-07-01	Agenda for the 7th Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-07-02	Minutes of the Sixth Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-07-03	Australian Department of Infrastructure and Transport & Transport Canada: Joint Australian and Canadian Pole Side Impact Research

PSI-07-04	Korea Automobile Testing & Research Institute: Evaluation of WS and ES2 Dummy in Pole Side Impact

PSI-07-05	Medical College of Wisconsin: Deflection Responses from PMHS in Oblique Side Impact Sled Tests

PSI-07-06	Medical College of Wisconsin & NHTSA Vehicle Research Test Centre: WorldSID Abdomen Tests

PSI-07-07	OICA: Proposal for PSI GTR Scope

PSI-07-08	OICA: Van and Passenger Car Dimensions

PSI-07-09	OICA: Preamble Text for Pole Side Impact Global Technical Regulation

PSI-07-10	Japanese Proposal for Narrow Vehicles (Kei Cars, Etc.) (Impact Velocity)

PSI-07-11	Beyond Safe – Bringing Physics into Models: Effect of Seating Height in Side Impact

PSI-07-12	RDW: Shoulder Loading of WorldSID 50th

PSI-07-13	BMW Group: WorldSID 50% Shoulder Assessment – Industry Proposal

PSI-08-01	Agenda for the 8th Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-08-02	Minutes of the Seventh Meeting of the GRSP Informal Group on a Pole Side Impact GTR

PSI-08-03	GTR on Pole Side Impact: Timetable

PSI-08-04	MUARC: Assessment of the Need for, and the Likely Benefits of, Enhanced Side Impact Protection in the Form of a Pole Side Impact Global Technical Regulation

PSI-08-05	OICA: Preamble to GTR Pole Side Impact Scope Discussions

PSI-08-06	OICA: GIDAS Accident Analysis Pole Side Impact with CVs

PSI-08-07	OICA: Proposed Scope

PSI-08-08	WorldSID 50th Injury Risk Curves

PSI-08-09	Rationale Behind the Shoulder Assessment Criteria for WorldSID

PSI-08-10	LAB: Pole Side Impact Cost/Benefit Study, French Data

PSI-08-11	Draft Text of the PSI Regulation

PSI-08-12	Draft Preamble – Global Technical Regulation No. XX Pole Side Impact

PSI-08-13	Lenard, J., Frampton, R., Kirk, A., Morris, A., Newton, R., Thomas, P., Fay, P.: Accidents, Injuries and Safety Priorities for Light Goods Vehicles in Great Britain.

PSI-08-14	Minutes of the Eighth Meeting of the GRSP Informal Group on a Pole Side Impact GTR

# Footnotes

* 	Conformément au programme de travail du Comité des transports intérieurs pour la période 2010-2014 (ECE/TRANS/208, par. 106, et ECE/TRANS/2010/8, activité 02.4), le Forum mondial a pour mission d’élaborer, d’harmoniser et de mettre à jour les Règlements en vue d’améliorer les caractéristiques fonctionnelles des véhicules. Le présent document est soumis dans le cadre de ce mandat.