| Submitted by the expert from Republic of Korea | Informal document GRSP-55-23 (55th GRSP, 19-25 May 2014, agenda item 19) |
| --- | --- |

Proposal of amendment to

ECE/TRANS/WP.29/GRSP/2014/8 (Proposal by European Commission and OICA of Draft Regulation on hydrogen and fuel cell vehicles)

I.	Proposal

Proposal, amend to read:

"Proposal for a new Regulation on hydrogen and fuel cell vehicles"

Title, amend to read:

"Draft Regulation on hydrogen and fuel cell vehicles"

Contents, amend to read:

"Uniform provisions concerning the approval of motor vehicles and their components with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles

Annexes 1

Part 1	Model I - Information document No … on the type approval of a hydrogen storage system with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles

Model II - Information document No … on the type approval of specific component for a hydrogen storage system with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles

Model III - Information document No … on the type approval of a vehicle with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles"

1. Scope, amend to read:

"1.1.	Part I - Compressed hydrogen storage systems for hydrogen-fuelled fuel cell vehicles on their safety-related performance."

"1.3.	Part III - Hydrogen-fuelled fuel cell vehicles of category M and N incorporating compressed hydrogen storage system on its safety-related performance."

2. Definitions, amend to read:

"2.12.	"Hydrogen-fuelled fuel cell vehicle" means any motor vehicle that uses compressed gaseous or liquefied hydrogen as a fuel to propel the vehicle, including fuel cell and internal combustion engine vehicles. Hydrogen fuel for passenger vehicles is specified in ISO 14687-2 and SAE J2719."

"2.14.	"Liquefied hydrogen storage system (LHSS)" means liquefied hydrogen storage container(s) PRDs, shut-off device, a boil-off system and the interconnection piping (if any) and fittings between the above components."

"2.1514.	... "

"2.2625.	...

(b)	the state of stored hydrogen fuel; compressed gas or liquefied;"

"2.2726.	...

(b)	the state of stored hydrogen fuel; compressed gas or liquefied;"

"2.29.	"Vehicle fuel system" means an assembly of components used to store or supply hydrogen fuel to a fuel cell (FC) or internal combustion engine (ICE)."

Annex 1 – Part 1, amend to read:

"Model I - Information document No … on the type approval of a hydrogen storage system with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles" ...

"Model II - Information document No … on the type approval of specific component for a hydrogen storage system with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles" ...

"Model III - Information document No … on the type approval of a vehicle with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles" ...

Annex 1 – Part 2, amend to read:

"Model I - Communication ... of a type of vehicle/component compressed hydrogen storage system with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles pursuant to Regulation No. XYZ ...

10. Approval with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles is granted/refused:"

...

"Model II - Communication ... of a type of specific component (TPRD / Check valve / Automatic shut-off valve  with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles pursuant to Regulation No. XYZ ...

10. Approval with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles is granted/refused:"

...

"Model I III - Communication ... of a type of vehicle with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles pursuant to Regulation No. XYZ ...

10. Approval with regard to the safety-related performance of hydrogen-fuelled fuel cell vehicles is granted/refused:" ...

II.	Justification

Aim of this proposal is to remove the contents of liquefied hydrogen storage system.