## Slide 1
Submitted by the Chair of the WLTP IWG | Informal document GRPE-70-20 70th GRPE, 13-16 January 2015 Agenda item 3(a)
Status report
of the
WLTP Informal Working Group
Report to the 70th GRPE session
by Stephan Redmann

## Slide 2
WLTP IWG Meetings since last GRPE
17-20 November 2014 8th WLTP IWG, Pune, India  Minutes WLTP-08-48e
14th January 2014 9th WLTP IWG, Geneva, Switzerland
 Minutes WLTP-09-29e
Continously Task force meetings, audio/web conferences

## Slide 3
Annex 1/2: Cycle & gear shifting issues
Status of WLTP phase 1B working items
Open issues table: WLTP-09-03e
Meeting minutes: WLTP-09-29e
Status report from H. Steven (WLTP-09-07e):
 Closed items:
Downscaling, use of gear box (def. nmax, Pwot), determination of engine speed, calculation of available power, 3s rule, gear shift family criteria, further improvments of gtr text.
On-going discussions: Use of gear box (def. nmin_drive), exclusion of aux. gears (crawler gear). Road load coeff. in gear shift calculation ( Annex 4 issue)
 Adoption foreseen at IWG #10.

## Slide 4
Annex 4: Road load and dynamometer setting
Annex 3: Reference fuels
 No phase 1B working items.
Status report from R. Cuelenaere: (WLTP-09-07e)
 Closed items:
Speed points, alternative warm up procedure, wheel alignement.
On-going discussions on key issues: - Wind tunnel / moving belt method
    Review on-board anemometry / wind conditions
    Review default road load parameters (combined default road load approach, adjustments for N1)
     Adoption foreseen at IWG #10.

## Slide 5
On-going discussions (cont.): - Road load family concept
    Review torque-meter method
 Closed items:
Review of 4WD specifications, Chassis dyno calibration aspects.
 All OIT items closed.
On-going:
    Review of (new) experts proposals, if necessary.
Annex 5: Test equipment and calibrations
Pending: - Tyre selection criteria of combined approach

## Slide 6
Annex 6: Test procedure and test conditions
 Closed items:
- Handling of Ki approach (most items) - Provisions for Coasting (WLTP-09-15e)
- Delayed progress, mainly because of fundamental discussions on “cycle modification” (reservations by EU, JPN)
- Time constraints, extensive data analysis necessary
 Working item closed for phase 1B
 Coasting technology will be reconsidered in WLTP phase 2 (strong interest of CLEPA)
 On-going discussions (key issues):
    Speed trace violations, Driving trace index (WLTP-06-16e)  Aim: Screening tool (SAE based methodology), „void test“ decision  Connected with correction algorithms proposal by EU COM

## Slide 7
 On-going discussions (cont.):
    Number of tests (WLTP-09-21-rev1e; incl. -22e) Aim: improve current GTR provisions from R83 (up to 3 tests)  1 or 2 tests with repetition criteria: [90] % of limit value.  Key points of discussion: - Different approach for CO2? (No limit values. Declared value.) - If no single CO2 test: repition criteria?

## Slide 8
Annex 7: Calculations
 Closed items:
FC calculation issues, FC interpolation method
Correction algorithms (WLTP-08-37e/-38e)
- Speed trace violations  Phase 1B: Drive Trace Index, Phase 2: Corrections. - Wheel alignment (RLD)  Solved: WLTP-09-10e. - Rotational inertia correction
     Objected, negative cost/benefit.
    - Inacc. of road load settings on chassis dyno
    Task Force RLD, probably solved in phase 1B.
    - Other issues: further investigations necessary.  Possibly WLTP phase 2 issues.

## Slide 9
 Closed items (cont.):
    Additional pollutants: Calculation formulas for Ammonia (NH3)
 On-going discussions (cont.):
    Additional pollutants: Calculation formulas for Ethanol & Aldehyde (Validation delayed due to measurement equipment availability)

## Slide 10
 Closed key item:
- Utility factors
1) Harmonized methodology in GTR to derive regional UF values
 reference to SAE standard 2) UFs based on regional choices (e. g. fleet / individual values)  overview of regional UFs will be given in GTR
 On-going discussions:
    - RCB Correction and phase specific calculation - Mode selectable switch - CO2 family and combined approach  Adoption IWG #10.
    - End of EV range criteria, PEV shortened test procedure, FCV test procedure
Annex 8: Pure and hybrid electric vehicles

## Slide 11
Reserved annex in GTR 15.
Objective: statistical procedure for comparison and validation of alternative measurement equipment and measurement procedures.
Similar regulations in GTR 4 (WHDC) and EPA 1066
 Review of existing regulations and adoption at IWG #10.
Annex 9: System equivalency

## Slide 12
General gtr issues:
 Drafting:
- New Subgroup „Drafting“, chaired by Drafting Coordinator.
- Tasks: Peer review of GTR (inconsistencies check), decisions on expert proposals (if possible), editorial review of task force / IWG proposals
 Definitions:
- VPSD recommendations, e.g. HEV definition - Review / transposition to WLTP GTR  Separate meeting of Subgroup „Drafting“.

## Slide 13
   Indication of temperatures °C / Kelvin (WLTP-09-19e) Based on DIN EN ISO 80000-5
  - Define 0° C as 273.15 K
  - Use “°C” for definition of temperatures - Use Kelvin (with .15) in calculations
  - Delete redundant information: ± 5 K (± 5 °C ) (Example)
   Recommendation: align other GTRs, e. g. EPPR
  Probably alignment of others? (kWh…)
 Round Robin Exercise
- European & Asian exercises are on-going. Finalization end of 2015.
- US EPA & China announced participation.
- EU: cross-over measurements with India, US.

## Slide 14
WLTP Phase 1b Roadmap
WP.29
GRPE
WLTP
2014 2015 2016
1 2 3 4 5 6 7 8 9 10 11 12 1 2 3 4 5 6 7 8 9 10 11 12 1 2 3 4 5 6
Fix organization, responsibilities
and time schedule
Phase2 ToR
5
6
7
8
9
10
gtr informal
document
Round Robin
167
168
169
71
73
70
72
69
68
gtr formal
document
Slight modification
11
12
13
Phase2
14

## Slide 15
WLTP Phase 2
Starting note by Japan, K. Kobayashi: WLTP-08-41-rev1e, incl. Questionnaire (WLTP-08-41-rev1e_annex)
Position on EV issues phase 2 & 3 by EU-COM (WLTP-08-42e (EVE-12-06e))
 Possible working items:
    Low ambient temperature
    High altitude test
    In-service conformity
    Durability
    Mobile air conditioning
    EV issues
Feedback by Contracting Parties (and other stakeholders) requested until end of February 2015

## Slide 16
WLTP IWG meetings in 2015
IWG #10 14.-16. April (EV Subgroup on 13th) Stockholm, Sweden
IWG #11 June GRPE, full day requested Geneva, Switzerland
IWG #12 September, dates t.b.d. Tokyo, Japan