## Slide 1: Environmental Control Technology Office, Policy Planning Division Environmental Management Bureau, Ministry of the Environment
Overview of the "Future Policy for Motor Vehicle Emission Reduction" (12th report presented by the Central Environment Council on Feb. 4, 2015)
International Harmonization of Exhaust Emissions Test Procedures for Passenger Vehicle (M1) and Light Trucks (N1)
1
Ministry of the Environment
Informal document GRPE-71-15
71st GRPE, 8 – 12 June 2015
Agenda items 3(b) and 16
Submitted by the expert from Japan the secretariat

## Slide 2
Contents
1. Introduction ・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・3
2. Key Points of the 12th Report ・・・・・・・・・・・・・・・・・・・・・・・・・6
3. Introducing the WLTP ・・・・・・・・・・・・・・・・・・・・・・・・・・・・・ ・ 7
4. Setting Permissible Exhaust Emission Limit Target Levels for the Next Term ・・・・・・・・・・ ・・・ ・・・ ・・・ ・・・ ・・・・・・・・・・・8
Ministry of the Environment

## Slide 3
The Central Environment Council successively has discussed the international harmonization of exhaust emissions test procedures, which led to the introduction of relevant regulations. (See the table on the right.)
International harmonization of exhaust emissions test procedures for Passenger Vehicles and Light Trucks remained to be discussed.
○ Recent Views of Discussion
In response to the inquiry made on May 21, 1996, the council presented a series of reports, from the interim report (in 1996) up to the 11th report (in 2012), and the vehicle emissions regulations have been tightened progressively .
As a result, enacted regulations are among the strictest in the world, contributing significantly to improving the atmospheric environment in Japan.
○ Overview of Previous Reports from the Central Environment Council
Reference: Previous Reports on the International Harmonization of Exhaust Emissions Test Procedures
International harmonization of exhaust emissions test procedures for Passenger Vehicles and Light Trucks remained and other subjects
○ Major topics in the 12th Report
1. Introduction
Report Title | Type of Regulated Vehicle
9th Report (Jan. 29, 2008) | Special diesels
10th Report (Jul. 28, 2010) | Heavy diesels
11th Report (Aug. 10, 2012) | Two-wheeled vehicles
12th Report (Feb. 4, 2015) | Passenger Vehicles and Light Trucks
Ministry of the Environment

## Slide 4
Course of Events
1. Introduction (continued)
2008・・・ GRPE under the UN-ECE/WP29 started formulating the WLTP-gtr.
2012・・・Cabinet meetings in 2012 determined that the Central Environment Council and other groups discuss the domestic implementation of the WLTP and the WLTP is introduced once a conclusion is reached.
Mar. 2014・・・The WLTP-gtr was adopted by the UN-ECE/WP29.
Apr. 2014・・・The Central Environment Council started discussing the implementation of the WLTP and other relevant subjects.
Feb. 2015・・・The Central Environment Council reported on the implementation of the WLTP and other relevant subjects.
Passenger vehicles and light trucks account for much of the four-wheeled vehicle production. For this reason, achieving the international harmonization of exhaust emissions test procedures for passenger vehicles and light trucks will significantly help protect the atmospheric environment, not only in Japan but in the rest of the world. It will also greatly help auto manufacturers to reduce the cost of developing emissions control technology and the workload required for the development.
Therefore, it is important to promptly achieve the international harmonization of exhaust emissions test procedures in the field of passenger vehicles and light trucks cars as well in order to reduce vehicle emissions. Cabinet meetings in 2012 determined that the Central Environment Council and other groups discuss the domestic implementation of the WLTP and the WLTP is introduced once a conclusion is reached.
Shortly after the WLTP-gtr was adopted by the UN-ECE/WP29, the Central Environment Council started discussing the domestic implementation of the WLTP and other relevant subjects.
After promptly finishing the discussion, the council reported on the domestic implementation of the WLTP and other relevant subjects this February.
Ministry of the Environment

## Slide 5
Air Pollution Control Act (Ministry of the Environment)
Exhaust emissions:
Permissible Limits on the vehicle emissions
Road Transport Vehicle Act
(Ministry of Land, Infrastructure, Transport and Tourism)
• Safety and environmental regulations for vehicles traveling on public roads
Reference: Review Process for Vehicle Emissions Regulations in Japan
Central Environment Council
Future Policy for Motor Vehicle Emission Reduction (inquired on May 21, 1996)
Inquiry from the Minister of the Environment to the Central Environment Council
Report from the Central Environment Council to the Minister of the Environment
Considered to ensure the permissible limits
Ministry of the Environment

## Slide 6
Ministry of the Environment
○ Setting the Permissible Exhaust Emission Limit Target Levels for the Next Term
Example: gasoline/LPG cars
 | Current | Next Term
CO | 1.15 | 1.15
NMHC | 0.05 | 0.10
NOx | 0.05 | 0.05
PM* | 0.005 | 0.005
[g/km]
Example: diesel cars
 | Current | Next Term
CO | 0.63 | 0.63
NMHC | 0.024 | 0.024
NOx | 0.08 | 0.15
PM | 0.005 | 0.005
[g/km]
• The UN-ECE/WP29 formulated the Worldwide Harmonized Light-Duty Test Cycle (WLTC). The WLTC provides different test cycles for Class 1, Class 2, Class 3a, and Class 3b vehicles to reflect the real-world driving situations in the individual CPs.
• The individual CPs have the option to exclude the extra-high-speed phase because it includes driving in the high acceleration, high-speed range.
• Test conditions are more stringent than before. (For example, cold start, test mass, running resistance .etc)
○ Details of the Worldwide Harmonized Light Vehicles Test Procedure (WLTP)
• It is recommended that the test cycles applied to Class 3a and Class 3b vehicles be adopted because these cycles match the driving situations in Japan. In these test cycles, the extra-high-speed phase, which does not match the driving situations in Japan will not adopted.
○ Introducing the WLTP
Key Points of the 12th Report
• Since the test cycles will be changed, we will review the current permissible exhaust emission limits. Although the limits on some substances seem to be set higher due to the stricter test conditions, those limits target levels are set not to relax the regulations.
• Only cold-start testing (100%) will be performed to evaluate exhaust emissions, which until now have been evaluated during both a cold and hot starts.
*Only applied to lean-burn direct-injection vehicles with an NOx absorber catalyst
Chart: Time (sec)
Equivalent to the current regulation level
2. Key Points of the 12th Report
Notes: A survey of real-world driving situations in Japan indicates that driving patterns that match the extra-high-speed phase account for only 5% of the total travel distance.
In addition, there is a large gap between the speed-acceleration distribution with the extra-high-speed phase and the speed-acceleration distribution that reflects the real-world driving situations in Japan. Meanwhile, in the case of the speed-acceleration distribution without the extra-high-speed phase, the gap is small.
Therefore, in the test cycles applied to Class 3a and Class 3b vehicles, we should exclude the extra-high-speed phase and adopt the low-, medium-, and high-speed phases shown in a separate figure (on page 28) for our exhaust emissions test procedures.

## Slide 7
Ministry of the Environment
Test Cycle (1): test cycle applied to Class 3a vehicles in the WLTP-gtr. (The extra-high-speed phase is excluded.)
Test Cycle (2): test cycle applied to Class 3b vehicles in the WLTP-gtr. (The extra-high-speed phase is excluded.)
3. Introducing the WLTP
Test Cycle (1)
Note: Different test cycles for vehicle types are assigned as shown in the table below.
Vehicle Type |  | Test Cycle
Gasoline/LPG mini-sized trucks | With maximum speeds below 120 km/h | Test Cycle (1)
 | With maximum speeds of 120 km/h or higher | Test Cycle (2)
Gasoline/LPG passenger cars, light-duty gasoline/LPG trucks, medium-duty gasoline/LPG trucks, diesel cars, light-duty diesel trucks, and medium-duty diesel trucks |  | Test Cycle (2)
Test Cycle (2)
It is recommended that the JC08 mode be changed to the WLTC applied to Class3a or Class 3b vehicles without ExH.

## Slide 8
4. Setting Permissible Exhaust Emission Limit Target Levels for the Next Term(1)
It is recommended that the permissible exhaust emission limit target levels for the next term are as shown on the next page, ensuring that the emission regulation levels are equivalent to the current Post-New Long-Term Regulations (established in 2009). These values also reflect the characteristics of the WLTP-gtr, such as a high-acceleration, high-speed range, test mass and cold-start emissions than in the current exhaust emissions test method based on the JC08 mode.
In the future, the values should be reviewed, if necessary, based mainly on the future effects of the regulations, the progress of technological developments, and the contribution of exhaust emissions. In its review, it is needed to take care to ensure that low-emission and fuel-efficient technologies can be achieved concurrently.
Ministry of the Environment

## Slide 9
○ Diesels
4. Setting Permissible Exhaust Emission Limit Target Levels for the Next Term (2)
Time of enforcement: These target values will come into effect in 2018 for passenger vehicles and light-duty trucks and in 2019 for medium-duty trucks.
Vehicle Type | Permissible Exhaust Emission Limit Target Levels |  |  | 
 | CO | NMHC | NOx | PM
Passenger vehicles | 0.63 g/km | 0.024 g/km | 0.15 g/km | 0.005 g/km
Light-duty trucks (gross vehicle weight ≤ 1.7 t) | 0.63 g/km | 0.024 g/km | 0.15 g/km | 0.005 g/km
Medium-duty trucks (1.7 t < gross vehicle weight ≤ 3.5 t) | 0.63 g/km | 0.024 g/km | 0.24 g/km | 0.007 g/km
○ Gasoline/LPG Vehicles
Time of enforcement: These target values will come into effect in 2018 for passenger vehicles and light-duty trucks and in 2019 for mini-sized trucks and medium-duty trucks.
Vehicle Type | Permissible Exhaust Emission Limit Target Levels |  |  | 
 | CO | NMHC | NOx | PM(Note)
Passenger vehicles | 1.15 g/km | 0.10 g/km | 0.05 g/km | 0.005 g/km
Mini-sized trucks | 4.02 g/km | 0.10 g/km | 0.05 g/km | 0.005 g/km
Light-duty trucks (gross vehicle weight ≤ 1.7 t) | 1.15 g/km | 0.10 g/km | 0.05 g/km | 0.005 g/km
Medium-duty trucks (1.7 t < gross vehicle weight ≤ 3.5 t) | 2.55 g/km | 0.15 g/km | 0.07 g/km | 0.007 g/km
Note: Only applied to gasoline-fueled lean-burn direct-injection vehicles with an NOx absorber catalyst.
Ministry of the Environment

## Slide 10
Thank you for your attention.
Ministry of the Environment