## Slide 1: 64th GRB
EU Regulation on AVAS requirements
Presentation by the European Commission expert
Transmitted by the expert from the European Commission
Informal document GRB-64-19
(64th GRB, 5-7 September 2016,
agenda item 11)

## Slide 2: Detailing requirements of Acoustic Vehicle Alerting System (AVAS)
2
  Commission empowered to detail by 1/7/2017 AVAS requirements that are already in Annex VIII to Reg. (EU) No 540/2014
  Commission Delegated Regulation taking into account the UNECE relevant work (UN R138 on QRTV)
Notes: 2

## Slide 3: UNECE Regulation No 138
3
M and N QRTVs concerned
  AVAS requirements included – only acoustic devices addressed to
  A) Technical
  Definitions, speed range of operation, min vehicle sound for at least two 1/3 octave bands, max vehicle sound 75 dB(A) in forward motion, frequency shift, tests for sound emission (forward and reverse), stationary sound (optional), AVAS pause function (switch): optional
  B) Administrative
  Type approval (procedures for application, modification, extension and related certificate and marking), CoP, penalties, Technical Services data
  Communication and marking models in Annexes 1 & 2
Notes: 3

## Slide 4: EU Regulation on AVAS requirements: Commission Delegated Regulation amending Regulation (EU) No 540/2014 of the European Parliament and of the Council as regards the Acoustic Vehicle Alerting System requirements for vehicle EU type-approval
4
Legal obligations:
to detail the requirements in Annex VIII by completing them only
to have the AVAS mandatory on all new EV and HEV types by 1/7/2019 and all new EV and HEV by 1/7/2021
Articles
Amendment of Annex VIII to Reg. 540/2014
Entry into force
Notes: 4

## Slide 5: EU Regulation on AVAS requirements
5
Annex
Based on the technical requirements drafting in Annex VIII, Reg. 540/2014
Completing the technical requirements of Annex VIII, Reg. 540/2014 by referring to requirements of UN R138
Copying the necessary admin requirements from UN R138
Notes: 5

## Slide 6: EU Regulation on AVAS requirements
6
Annex (cont'd)
A) Technical requirements
Accepting from UN R138 the definitions of "Pause function" and "Frequency shift"
The AVAS sound generation requirement in forward motion and reverse as in Reg. 540/2014
+ from UN R138: requirements on testing, min vehicle sound level and frequency shift when no AVAS in reverse, due to vehicle warning alarm
Notes: 6

## Slide 7: EU Regulation on AVAS requirements
7
    Annex (cont'd)
    Pause switch
    From UN R138
    + Pause function (new term)
    + Optional – to be amended following the UN Reg. final decision
    + Complying with the requirements in UN R138
    Attenuation
    Requirement from Reg. 540/2014
    + from UN R138 : min sound level & frequency shift
Notes: 7

## Slide 8: EU Regulation on AVAS requirements
8
    Annex (cont'd)
    Sound produced
    As in Reg. 540/2014
Continuous to warn pedestrians and other road users
Indicative of the vehicle operation
From UN R138:
+ Frequency shift
+ Optional stationary noise, complying with the attenuation requirements of this Regulation, if attenuated
+ Driver selectable sounds
Notes: 8

## Slide 9: EU Regulation on AVAS requirements
9
    Annex (cont'd)
    Sound volume
    As in Reg. 540/2014
+ from UN R138: overall vehicle sound level 75 dB(A) in forward motion
    Transitional provisions
+ On test track: from ISO 10844:1994 (till 30 June 2019) to ISO 10844:2014
(from UN R138)
Notes: 9

## Slide 10: EU Regulation on AVAS requirements
10
    Annex (cont'd)
    B) Administrative requirements copied from the UN R138
+ Communication (type-approval certificate ) & its model
+ Marking on vehicle & its model
Notes: 10

## Slide 11: Next steps
11
    First comments from MVWG done
    New draft incorporating comments September 2016
    Discussion of new draft in dedicated MSEG and / or
    comments in writing October 2016
    ISC end 2016-start 2017
    Adoption Q1 2017
Notes: 11

## Slide 12: Thank you for your attention DG GROW – Unit C4
Further information:
http://ec.europa.eu/growth/sectors/automotive/index_en.htm