## Slide 1: Strengthening Tyre limits ! New developments (2)
Johan Sliggers, Ministry of Transport & Environment Netherlands
Transmitted by the expert from the Netherlands
Informal document GRB-68-27
(68th GRB, 12-14 September 2018,
agenda item 6)

## Slide 2: 1. New EU proposal Regulation General Safety
Proposal for a REGULATION OF THE EUROPEAN PARLIAMENT AND OF THE COUNCIL on type-approval requirements for motor vehicles and their trailers, and systems, components and separate technical units intended for such vehicles, as regards their general safety and the protection of vehicle occupants and vulnerable road users, amending Regulation (EU) 2018/… and repealing Regulations (EC) No 78/2009, (EC) No 79/2009 and (EC) No 661/2009

## Slide 3: Article 1 Subject matter This Regulation establishes requirements:
3. for the type-approval of newly-manufactured tyres with regard to their safety and environmental performance.

## Slide 4: Article 4 General obligations and technical requirements
2. Type-approval in accordance with the UN Regulations listed in Annex I shall be considered as EU type-approval in accordance with the requirements of this Regulation and of the delegated acts adopted pursuant to it.
ANNEX I List of UN Regulations referred to in Article 4(2)
Regulation117: Tyres with regard to rolling sound emissions, adhesion on wet surfaces and rolling, Supplement 8 to the 02 series of amendments, Vehicle types M, N, O

## Slide 5: Tyres in Europe
GRB-66-01 (Netherlands) Tyres in Europe
GRB-66-01-Add.1 (Netherlands) Tyres in Europe
Benefits of strengthening the limits in two stages (stage 3 and 4)
Perspective Europe (EU):
  511 million people, 293 million cars

## Slide 6: Rolling Resistance coefficient (N/kN)
Tyre type | Current limit | Stage 3 | Stage 4
C1 | 10.5 | 9.0 | 8.0
C2 | 9.0 | 8.0 | 7.0
C3 | 6.5 | 6.0 | 5.5

## Slide 7: Wet Grip index (G)
Tyre type | Current limit | Stage 3 | Stage 4
C1 | 1.1 | 1.45 | 1.6
C2 | 0.95 | 1.25 | 1.35
C3 | 0.80 | 1.1 | 1.2

## Slide 8: Noise (rolling sound emissions dB(A))
Tyre type | Current limit | Stage 3 | Stage 4
C1 | 70-74 | 69-73 | 67-71
C2 | 72 | 71 | 70
C3 | 73 | 71 | 69

## Slide 9: Potential benefits Stage 3, 4 and Proper tyre pressure in the EU
 | Stage 4 limits | Stage 3 limits | Proper pressure
Fuel savings [billion l/yr] | 17 | 8 | 5
CO2 reduction [Mt/yr] | 42 | 21 | 12
Reduced # of fatalities | 2567 | 1300 | 140
Reduced # of slight/ serious injuries | 19631/ 12353 | 10000/ 6000 | 1100/ 7000
Reduced # of annoyed people [millions] | 13 | 6 | 1.5
Reduced # of sleep disturbed people [mill.] | 6 | 3 | 0.6
Cost savings [billion €/y] | 34 | 17 | 6

## Slide 10: Strengthening the tyre limits is profitable
For countries
For car owners
For civilians

## Slide 11: 2. Working Group on Noise and Tyres (GRBP) Noblesse Oblige !
Request Netherlands to GRBP:
  Transform Informal doc GRB-66-03: Proposal for amendments to the 02 series of amendments to Regulation No. 117, into a
Working Document for GRB, January 2019

## Slide 12: Thank you for your attention !